Atmel Atmega128 Overview
ALU Particulars
RISC Architecture
133, Mostly single cycle instructions
2 Address instructions (opcode, Rs, Rd, offset)
32x8 Register file
-6 can be used as 16-bit registers
Harvard architecture
Status Register
(half carry, sign, OV, Neg, Zero, Carry, GIE)
-not stored when entering ISR

---
Memory System
There are four separate memory spaces on the AVR
-Program space:
-128K byte (64Kx16) in-circuit flash programmable
-Endurance minimum of 10K cycles
-Can be accessed by program for storage of constants
-SRAM Data Memory:
-4K bytes
-variable storage area
-i/o and peripherals are located here also
-EEPROM:
-4K bytes
-separate data space
-single byte read/write access via EEPROM access registers
-8.5mS to write data (slow but durable)

---
Memory System
-Mega128 board has added 32K external SRAM memory
-Uses multiplexed lower address and data
-Addr bit 15 selects external memory if XMEM register is programmed

---
Timers and Counters
TCNT0
-8-bit
-internal synchronous clock or external asynchronous 32Khz clock
-especially used for time keeping with 32Khz clock
-has no external pin for clocking, only two crystal sources

---
Timers and Counters
TCNT1, TCNT3
-16 bit timer/counter, requires special access method
-clocked by internal clock or by external pin
-3 output compare registers and output pins (set, reset, toggle)
-multiple compare registers
-input capture register captures when external event happened
-ADC interrupt input can capture time at which some voltage is detected

---
Timers and Counters
TCNT1, TCNT3

---
Timers and Counters
TCNT2
-8-bit counter/timer
-like TCNT0 but has external clocking capability
-has PWM capability

---
Timer/counter prescalers
-separate prescalers available for TCNT1,2,3 only
-used when operating from internal or external clock pin
-clock can be prescaled by 8, 64, 256 or 102

---
Interrupts
 30 interrupt sources
-external pin levels or edges
-timer/counters
-SPI, USART, and TWI Rx and Tx complete
-ADC conversion complete
-EEPROM ready
-input capture, external event capture, ADC interrupt
All interrupts are vectored
-reset is vector zero (highest priority)
-all other interrupts are prioritized in ascending order
-interrupt response time is 4 cycles
-interrupt return time is also 4 cycles

---
Serial Interfaces
SPI (Serial Peripheral Interface)
-full duplex, three wire interface
-MSB first or last, programmable bit rates to clock/2

---
Serial Interfaces
USART(universal synchronous asynchronous receiver transmitter)
-2 identical and separate units, USART0, USART1
-full duplex serial communications
-programmable number of bits, parity, stop bit, error detection
-interrupt on tx done, rx ready, or tx register empty

---
Serial Interfaces
USART0,1

---
Serial Interfaces
TWI (two wire interface)
-half duplex serial communications
-7 bit device addressing
-multi-master operation
-400khz data rate
-I2C compatible

---
Analog to Digital Converter
-10-bit resolution
-13-260uS conversion time
-8 multiplexed single input channels
-7 differential input channels
-selectable internal reference (2.56V)
-input range 0-Vcc
-interrupt on completion

---
Analog to Digital Converter