Debouncing Switches
Mechanical switches are one of the most common interfaces to a uC.
Switch inputs are asynchronous to the uC and are not electrically clean.
Asynchronous inputs can be handled with a synchronizer (2 FF's).
Inputs from a switch are electrically cleansed with a switch debouncer.
What is switch bounce?
-The non-ideal behavior of the contacts that creates multiple electrical	transitions for a single user input.

---
Switch bounce from a single depress/release of mega128 pushbutton switches

---
The problem is that the uC is usually fast enough to see all the transitions
-uC acts on multiple transitions instead of a single one
The oscilloscope traces showed bounce durations of 10-300us
-our mega128 uC runs at 62.5ns per instruction
-a 10uS bounce (short) is (1x10-5/62.5x10-9) 160 instructions long!
-a 100uS bounce could be sampled as a valid true or false 100’s of times
-results are incorrect behavior as seen by user
Characteristics of switch bounce:
-nearly all switches do it
-the duration of bouncing and the period of each bounce varies
-switches of exactly the same type bounce differently
-bounce differs depending on user force and speed
-typical bounce frequency is .1-5ms
Effective switch debouncing can also reject EMI and static charge effects
-EMI can be periodic (so don't sample synchronously!)
-false triggering on static electricity is like a single random input

---
Solutions
-Analog filtering
-usually an RC delay to filter out the rapid changes in switch output
-task is to choose R and C such that the input threshold is not crossed
while bouncing is still occurring
in
in
out
Vth
0V
out
0V

---
Solutions
-Cross coupled gates (MC14044)
-logic gates lock in one transition with a single-pole, double-throw switch
-both switch ($3.69) and chip ($0.38) are expensive
-momentary click switches (mega128 board) are ($0.12)
Vdd
Vdd

---
Solutions:
-Software
-need to minimize CPU usage
-independent of clock speed
-do not connect to interrupt pins, only programmed I/O
-multiple interrupts will tie up processor
-don't scan synchronously to noisy devices
-identify initial switch closure quickly (100mS max)
-Two approaches (of many)
-Count based
(identify initial closure AND wait AND check for same value) OR
(identify initial closure AND check for same value for X cycles)
-watch for
-CPU speed dependencies (use constant defines)
-loop execution times (suggesting the use of timer interrupts)
-Digital filter based
-mimics an analog filter with first-order recursive low pass filter
-includes a software schmitt trigger
-good EMI filtering, quick response
risky!
safer!

---
Solutions:
-Count based
-from Gansel's “Guide to Debouncing”
-routine called from timer interrupt or delay loop
-check Port D, bit 2, pushbutton depression, (bit will be grounded)
-returns “1' only once per button push, “pulsed output”
-looks for a falling edge
int8_t debounce_switch() {
  static uint16_t state = 0; //holds present state
  state = (state << 1) | (! bit_is_clear(PIND, 2)) | 0xE000;
  if (state == 0xF000) return 1;
  return 0;
  }
  value of state
first pass after reset:	1110 0000 0000 0001	return 0
second pass after reset:	1110 0000 0000 0011	return 0
after 12 false passes:	1111 1111 1111 1111	return 0
after 7 true passes:	1111 1111 1000 0000	return 0
after 12 true passes:	1111 0000 0000 0000	return 1
after many true passes:	1110 0000 0000 0000	return 0
after 5 false passes:	1110 0000 0001 1111	return 0

---
Solutions:
-Digital filter based
-acts like analog RC filter followed by schmitt trigger
-nearly continuous output like an analog circuit
- 0.25= 0x3F, 0.75=0xC0, 1.0 = 0xFF
uint8_t output=0; //external variable indicating switch state
uint8_t debounce_switch2() {
  static uint8_t y_old=0, flag=0;
  uint8_t temp;
//digital filter part y_old = x_new*0.25 + y_old*0.75
  temp = (y_old >> 2); //this gives y_old/4
  y_old = y_old – temp; //do (y_old*0.75) by subtraction
//if button is pushed, add 0.25 (3F) of new value (1.0)
  if(bit_is_clear(PIND, 2)){y_old = y_old + 0x3F;} //
//software schmitt trigger
  if((y_old > 0xF0)&&(flag==0)){flag=1; output=1;}
  if((y_old < 0x0F)&&(flag==1)){flag=0; output=0;}
}

---
Behavior of the digital filter debounce with schmitt trigger

---
Using Others Code
I just showed you several code snippets that you can use.
You should understand how they work.
You may (wink, wink) probably be tested on them in the future.
I offer other pieces of code in the coming weeks.
Learn what they do before you use them.
In general, don't use code from somewhere else without knowing how it works.
An exception would be a well used, well tested library of functions (libc).

---
Types of debouncer output
Sometimes we want a continuous output, e.g., organ keyboard.
Other times we want a pulsed output, e.g. increment hour alarm.
The first counting algorithm (Gansel) gives a pulsed output.
The digital filter algorithm gives a continuous output.
button push
pulsed output
continuous output

---
Converting between types of debouncer output
To get a pulsed output, from a continuous debouncer:
output = 1
pushed
pushed=1
output = 0
always
idle
output = 0
waiting
pushed=0

---
Converting between types of debouncer output
To get a continuous output, from a pulsed output:
Note that this requires sensing rising and falling edges.
pushed=rising edge
output = 0
output = 1
idle
pushed
pushed=falling edge