PowerPoint Presentation
8-Bit Timer/Counter 0
Counter/Timer 0 and 2 (TCNT0, TCNT2) are nearly identical.
Differences:
-TCNT0 can run off an external 32Khz clock (Tosc) or the internal clock
 after it has passed through the prescaler.
-TCNT2 can run off of an external or the internal clock.
Since TCNT0 can run off a clock asynchronous to the CPU, some issues occur:
-control register writes are delayed by two Tosc edges, @ 32Khz, = 61uS!
-entering power save modes must be delayed after writing control registers
-async clock may take up to 1sec to stabilize at power up
32Khz crystal

---
Counters, timers, PWM generators are all easily implemented.
Two interrupt sources exist
-overflow (counter register over or under flows)
-output compare (counter register = compare register)
TCNT0 can be clocked internally or by an external 32Khz clock.
The external clock oscillator is optimized for 32.768 Khz watch crystals.
Applying a 32.768 Khz oscillator output to the Tosc pins is not recommended.

---
Four Registers: TCNT0, OCR0, TCCR0, ASSR
-TCNT0: (timer/counter register)
-the 8-bit counter itself
-holds the present value of count
-OCR0: (output compare register)
-this register is always compared against TCNT0
-TCCR0: (timer/counter 0 control register)
-determines the mode of operation
-ASSR: (asynchronous status register)
-coordinates writing to TCNT0, OCR0, TCCR0 when in
asynchronous mode

---
Timer/Counter 0 Clock Sources:
-AS0 bit in ASSR determines if clock source is internal or external
-internal clock is fclk @ 16Mhz
-external clock is Tosc @ 32Khz
Once choice of clock is made, it may be divided by the prescaler by
-8, 64, 256, or 1024
If no clock is selected, the timer is stopped and disabled.

---
Output Compare Unit:
-8-bit comparator continuously compares TCNT0 and OCR0.
-If equal, the output compare flag is set (OCF0) and an interrupt can be issued.
-The waveform generator uses this signal to generate an output to a pin.

---
Modes of Operation:
Determined by
-waveform generation mode (WGM01:0)
-compare output mode (COM01:0)
Normal Mode (WGM1:0 =0)
-simplest mode
-count up to TOP @ 0xFF and wrap to BOTTOM @ 0x00
-TOV0 flag is set when the wrap around occurs (overflow)
-to reset TOV0, ISR must be executed or flag manually cleared
-no output pins are enabled

---
Modes of Operation:
Clear Timer on Compare Match (CTC) Mode (WGM1:0 =2)
-counter resolution manipulated by output compare register (OCR0)
-counter cleared to zero when its value equals OCR0
-TOP defined by OCR0
-interrupt can be generated at compare point
-output pin (OC0) can be utilized
-output pin can toggle, set, or clear on match
-duty cycle constant, frequency is variable
OCR0=0xF000
OCR0=0x7F00
OCR0=0x00FF
OCR0=0x003F
note: fixed duty cycle, variable frequency

---
Modes of Operation:
Fast PWM Mode (WGM1:0 =3)
-used to create high resolution PWM waveforms
-same frequency, different duty cycle
-count from BOTTOM to 0xFF, then reset to BOTTOM
-output compare behaviour:
-set on compare match
-reset at TOP
-TOP is defined by OCR0
-limited to 7 different PWM frequencies
compare value sets duty cycle
value of TOP sets frequency
note: fixed frequency, variable duty cyele

---
Code examples
// tcnt0_normal.c
// setup TCNT0 in normal mode and blink PB0 LED at 1 sec intervals
// blink frequency = (32768)/(2^8 * 64 * 2) = 1.000000 blinks per sec
//
#include <avr/io.h>
int main()
{
  uint8_t count=0;
  DDRB = 0x01; //set port B bit zero to output
  ASSR |= (1<<AS0); //use ext oscillator
  TCCR0 |= (1<<CS00); //normal mode, no prescaling
  while(1) {
    while (! (TIFR & (1<<TOV0))){} //spin till overflow
      TIFR |= (1<<TOV0); //clear by writing a one to TOV0
      count++; //extend counter
      //toggle PB0 every 64 overflows
      if((count % 64) == 0){PORTB ^= 0x01;}
  } //while
} // main

---
Code examples
// tcnt0_normal_int.c
// use interrupts now
// setup TCNT0 in normal mode and blink PB0 LED at 1 sec intervals
// blink frequency = (32768)/(2^8 * 64) = 1.000000 blinks per sec
//
#include <avr/io.h>
#include <avr/interrupt.h>
ISR(TIMER0_OVF_vect){
  static uint8_t count=0; //hold value of count between interrupts
  count++; //extend counter
  //toggle PB0 each time this happens
  if((count % 64) == 0){PORTB ^= 0x01;}
}//TIMER0_OVF_vect
int main() {
  DDRB = 0x01; //set port B bit zero to output
  TCCR0 |= (1<<CS00); //normal mode, no prescaling
  ASSR |= (1<<AS0); //use ext oscillator
  TIMSK |= (1<<TOIE0); //allow interrupts on overflow
  sei(); //interrupts turned on
  while(1) {} //spin forever waiting on interrupts
  //(note nearly empty main, no need for volatile count variable)
} // main