Using avr-libc
avr-libc provides a subset of the standard C library for AVR microcontrollers.
avr-libc also provides necessary startup code for most applications.
Details (oh, are there details) are linked from the class web page at:
Many categories of libc modules to make embedded programming easier:
-Delay loops
-EEPROM access
-character operations
-integer conversions
-math operations
-string operations
-interrupts
http://www.nongnu.org/avr-libc/user-manual/index.html

---
More examples using avr-libc
Character operations...
#include <string.h>
//right justify results on the LCD
for(i=0; i<=(14–(strlen(lcd_str) + strlen(lcd_str1))); i++)
 char2lcd(‘ ‘);
Fake floating point math and print results
#include <stdlib.h>
div_t fp_adc_result, fp_low_result; //double fp_adc_result;
fp_adc_result = div(adc_result, 205); //should be 204.8 to be exact
low = fp_adc_result.rem;
high = fp_adc_result.quot;
fp_low_result = div((low*100), 205); //set decimal fraction
itoa(fp_low_result.quot, lcd_str, 10); //convert to ascii string
itoa(high, lcd_str1, 10); //convert to ascii string
Convert integers to ascii scring

---
Examples using avr-libc
Character conversion:
Setup a interrupt service routine. The ISR created will save registers for you
and will disable interrupts when entering the ISR.
#include <stdlib.h>
itoa(frequency, lcd_freq_str, 10); //convert integer to ASCII string
#include <avr/interrupt.h>
/***********************************************************************/
// timer/counter 1 ISR
//When the TCNT1 compare1A interrupt occurs, port F bit 4 is toggled.
//This creates the alarm sound from the clock.
/***********************************************************************/
ISR(TIMER1_COMPA_vect){
     if (alarm_enable == 1) //toggle port F bit 4 if valid button pushed
       PORTF ^= 0x10;
}//ISR

---
Generating timing delays:
Note: compiler optimizations must be enabled and the delay time must be an expression that is a known constant at compile-time.
#define F_CPU must be defined as a constant. It defines the CPU clock frequency (in Hertz).
The maximal possible delay is 262.14 ms / F_CPU in MHz. If the user requests more delay, resolution is limited to 0.1mS and user will not be notified. See avr-libc Function Documentation for details.
There is also a _delay_us function for smaller delays.
#define F_CPU 16000000UL //16Mhz
#include <util/delay.h>
for(i=0; i<=3; i++) {_delay_ms(250);} //delay for 1 sec

---
Accessing EEPROM memory:
#include <avr/eeprom.h>
/***********************************************************************/
// save_settings
//Saves user settings into EEPROM when power is going down.
void save_settings(){
  eeprom_write_byte(&eeprom_alarm_volume, alarm_volume);
  eeprom_write_byte(&eeprom_alarm_level, alarm_level);
}//save_settings
/***********************************************************************/