ECE 375 Lab 1

Introduction to AVR Development Tools

Lab Time: Tuesday 4-6

John Doe

Jane Row

# Introduction

Text goes here. Here we give you an example, please read through and remove it for your version. The lab write-up should be done in the style of a professional report/white paper.  Proper headers need to be used and written in a clean, professional style.  Proof read the report to eliminate both grammatical errors and spelling.  The introduction should be a short 1-2 paragraph section discussing what the purpose of this lab is.  This is not merely a copy from the lab handout, but rather your own personal opinion about what the object of the lab is and why you are doing it.  Basically, consider the objectives for the lab and what you learned and then briefly summarize them.  For example, a good introduction to lab 1 may be as follows.

The purpose of this first lab is to provide an introduction on how to use AVRStudio4 software for this course along with connecting the AVR board to the TekBot base.  A simple pre-made “BumpBot” program was provided to practice creating a project in AVRStudio4, building the project, and then using the Universal Programmer to download the program onto the AVR board.

# Program Overview

Text goes here. Here we give you an example, please read through and remove it for your version. This section provides an overview of how the assembly program works.  Take the time to write this section in a clear and concise manner.  You do not have to go into so much detail that you are simply repeating the comments that are within your program, but simply provide an overview of all the major components within your program along with how each of the components work.  Discuss each of your functions and subroutines, interesting program features such as data structures, program flows, and variables, and try to avoid nitty-gritty details.  For example, simple state that you “First initialized the stack pointer,” rather than explaining that you wrote such and such data values to each register.  These types of details should be easily found within your source code.  Also, do not hesitate to include figures when needed.  As they say, a picture is worth a thousand words, and in technical writing, this couldn’t be truer.  You may spend 2 pages explaining a function which could have been better explained through a simple program-flow chart.  As an example, the remainder of this section will provide an overview for the basic BumpBot behavior.

The BumpBot program provides the basic behavior that allows the TekBot to react to whisker input.  The TekBot has two forward facing buttons, or whiskers, a left and a right whisker.  By default the TekBot will be moving forward until one of the whiskers are triggered.  If the left whisker is hit, then the TekBot will backup and then turn right for a bit, while a right whisker hit will backup and turn left.  After the either whisker routine completes, the TekBot resumes its forward motion.

Besides the standard INIT and MAIN routines within the program, three additional routines were created and used.  The HitRight and HitLeft routines provide the basic functionality for handling either a Right or Left whisker hit, respectively.  Additionally a Wait routine was created to provide an extremely accurate busy wait, allowing time for the TekBot to backup and turn.

## Initialization Routine

Text goes here. Here we give you an example, please read through and remove it for your version. The initialization routine provides a one-time initialization of key registers that allow the BumpBot program to execute correctly.  First the Stack Pointer is initialized, allowing the proper use of function and subroutine calls.  Port B was initialized to all outputs and will be used to direct the motors.  Port D was initialized to inputs and will receive the whisker input.  Finally, the Move Forward command was sent to Port B to get the TekBot moving forward.

## Main Routine

Text goes here. Here we give you an example, please read through and remove it for your version. The Main routine executes a simple polling loop that checks to see if a whisker was hit.  This is accomplished by first reading 8-bits of data from PINE and masking the data for just the left and right whisker bits.  This data is checked to see if the right whisker is hit and if so, then it calls the HitRight routine.  The Main routine then checks to see if the left whisker is hit and if so, then it calls the HitLeft routine.  Finally a jump command is called to move the program back to the beginning of the Main Routine to repeat the process.

## Subroutines

- HitRight Routine

Text goes here. Here we give you an example, please read through and remove it for your version. The HitRight routine first moves the TekBot backwards for roughly 1 second by first sending the Move Backwards command to PORTB followed by a call to the Wait routine.  Upon returning from the Wait routine, the Turn Left command is sent to PORTB to get the TekBot to turn left and then another call to the Wait routine to have the TekBot turn left for roughly another second.  Finally, the HitRight Routine sends a Move Forward command to PORTB to get the TekBot moving forward and then returns from the routine.

- HitLeft Routine

Text goes here. Here we give you an example, please read through and remove it for your version. The HitLeft routine is identical to the HitRight routine, except that a Turn Right command is sent to PORTB instead.  This then fills the requirement for the basic BumpBot behavior.

- Wait Routine

Text goes here. Here we give you an example, please read through and remove it for your version.  The Wait routine requires a single argument provided in the waitcnt register.  A triple-nested loop will provide busy cycles as such that  cycles will be executed, or roughly .  In order to use this routine, first the waitcnt register must be loaded with the number of 10ms intervals, i.e. for one second, the waitcnt must contain a value of 100.  Then a call to the routine will perform the precision wait cycle.

# Additional Questions

Text goes here. Here we give you an example, please read through and remove it for your version. Almost all of the labs will have additional questions. Use this section to both restate and then answer the questions.  Failure to provide this section when there are additional questions will result in no points for the questions.  Note that if there are no Additional Questions, this section can be eliminated.  Since the original lab does not have any questions, I will make some up to illustrate the proper formatting.

1) Should your lab write-up discuss a narrative of how you accomplished the lab?

No! Remember that this is a professional report and a narrative comment such as “First we downloaded the lab handout and then the skeleton code.  We then followed the TAs instructions…” should not be used within this report.  Simply describe how your program behaves and answer the questions will suffice.

2) What is the purpose of creating a professional Lab report?

Until this class, most students have only been exposed to Technical Writing during Technical Writing course.  Since this is a Junior level course, this means that you are close to graduating an entering into the work force or doing an internship.  During this time, when your boss requests a report, he/she is expecting a professionally written report.  Remember that as engineers, we are expected to be and act professional.  So, by requiring you to write these lab reports, you are gain valuable experience need to write professionally.

# Difficulties

Text goes here. Here we give you an example, please read through and remove it for your version. This section is entirely optional.  Your grade does not depend on it.  But it is recommended that, if you had difficulties of some sort, list them here and how you solved them.  By documenting your “bugs” and “bug fixes”, you can then quickly go back to these sections in the event that the same bug occurs again, allowing you to quickly fix the problem.  An example difficulty may be:

Upon loading the program into the TekBot, the TekBot was turning left instead of forward.  The problem was a wiring issue with the left motor as the left direction and enable wires were crossed.  By swapping the wires, the Left Motor began moving forward and the problem was fixed.

# Conclusion

Text goes here. Here we give you an example, please read through and remove it for your version. The conclusion should sum up the report along with maybe a personal though on the lab.  For example, in this lab, we were simply required to set up an AVRStudio4 project with an example program, compile this project and then download it onto our TekBot bases.  The result of this program allowed the TekBot to behave in a BumpBot fashion.  The lab was great and allowed us the time to build the TekBot with the AVR board and learn the software for this lab.

# Source Code

Provide a copy of the source code.  Here you should use a mono-spaced font and can go down to 8-pt in order to make it fit.  Sometimes the conversion from standard ASCII to a word document may mess up the formatting.  Make sure to reformate the code so it looks nice and is readable.

;***********************************************************

;*

;*	BasicBumpBot.asm	-	V1.0

;*

;*	This program contains the neccessary code to enable the

;*	the TekBot to behave in the traditional BumpBot fashion.

;*	It is written to work with the v1.03 TekBots plateform.

;*	For v1.02 TekBots, comment and uncomment the appropriate

;*	code in the constant declaration area as noted.

;*

;*	The behavior is very simple.  Get the TekBot moving

;*	forward and poll for whisker inputs.  If the right

;*	whisker is activated, the TekBot backs up for a second,

;*	turns left for a second, and then moves forward again.

;*	If the left whisker is activated, the TekBot backs up

;*	for a second, turns right for a second, and then

;*	continues forward.

;*

;***********************************************************

;*

;*	 Author: David Zier

;*	   Date: March 29, 2003

;*	Company: TekBots(TM), Oregon State University - EECS

;*	Version: 1.0

;*

;***********************************************************

;*	Rev	Date	Name		Description

;*----------------------------------------------------------

;*	-	3/29/02	Zier		Initial Creation of Version 1.0

;*

;*

;***********************************************************

.include "m128def.inc"			; Include definition file

;************************************************************

;* Variable and Constant Declarations

;************************************************************

.def	mpr = r16				; Multi-Purpose Register

.def	waitcnt = r17				; Wait Loop Counter

.def	ilcnt = r18				; Inner Loop Counter

.def	olcnt = r19				; Outer Loop Counter

.equ	WTime = 100				; Time to wait in wait loop

.equ	WskrR = 4				; Right Whisker Input Bit

.equ	WskrL = 5				; Left Whisker Input Bit

.equ	EngEnR = 4				; Right Engine Enable Bit

.equ	EngEnL = 7				; Left Engine Enable Bit

.equ	EngDirR = 5				; Right Engine Direction Bit

.equ	EngDirL = 6				; Left Engine Direction Bit

;/////////////////////////////////////////////////////////////

;These macros are the values to make the TekBot Move.

;/////////////////////////////////////////////////////////////

; Move Forwards Command

.equ	MovFwd = (1<<EngDirR|1<<EngDirL)

.equ	MovBck = $00		; Move Backwards Command

.equ	TurnR = (1<<EngDirL)	; Turn Right Command

.equ	TurnL = (1<<EngDirR)	; Turn Left Command

; Halt Command

.equ	Halt = (1<<EngEnR|1<<EngEnL)

;============================================================

; NOTE: Let me explain what the macros above are doing.

; Every macro is executing in the pre-compiler stage before

; the rest of the code is compiled.  The macros used are

; left shift bits (<<) and logical or (|).  Here is how it

; works:

;	Step 1.  .equ	MovFwd = (1<<EngDirR|1<<EngDirL)

;	Step 2.		substitute constants

;			 .equ	MovFwd = (1<<5|1<<6)

;	Step 3.		calculate shifts

;			 .equ	MovFwd = (b00100000|b01000000)

;	Step 4.		calculate logical or

;			 .equ	MovFwd = b01100000

; Thus MovFwd has a constant value of b01100000 or $60 and any

; instance of MovFwd within the code will be replaced with $60

; before the code is compiled.  So why did I do it this way

; instead of explicitly specifying MovFwd = $60?  Because, if

; I wanted to put the Left and Right Direction Bits on different

; pin allocations, all I have to do is change thier individual

; constants, instead of recalculating the new command and

; everything else just falls in place.

;==============================================================

;**************************************************************

;* Beginning of code segment

;**************************************************************

.cseg

;--------------------------------------------------------------

; Interrupt Vectors

;--------------------------------------------------------------

.org	$0000			; Reset and Power On Interrupt

rjmp	INIT		; Jump to program initialization

.org	$0046			; End of Interrupt Vectors

;--------------------------------------------------------------

; Program Initialization

;--------------------------------------------------------------

INIT:

; Initilize the Stack Pointer (VERY IMPORTANT!!!!)

ldi	mpr, low(RAMEND)

out	SPL, mpr	; Load SPL with low byte of RAMEND

ldi	mpr, high(RAMEND)

out	SPH, mpr	; Load SPH with high byte of RAMEND

; Initialize Port B for output

ldi	mpr, $00	; Initialize Port B for outputs

out	PORTB, mpr	; Port B outputs low

ldi	mpr, $ff	; Set Port B Directional Register

out	DDRB, mpr	; for output

; Initialize Port E for inputs

ldi	mpr, $FF	; Initialize Port E for inputs

out	PORTE, mpr	; with Tri-State

ldi	mpr, $00	; Set Port E Directional Register

out	DDRE, mpr	; for inputs

; Initialize TekBot Foward Movement

ldi	mpr, MovFwd	; Load Move Foward Command

out	PORTB, mpr	; Send command to motors

;---------------------------------------------------------------

; Main Program

;---------------------------------------------------------------

MAIN:

in	mpr, PINE	; Get whisker input from Port D

andi	mpr, (1<<WskrR|1<<WskrL) ; Mask the whiskers

cpi	mpr, (1<<WskrR); Check for Right Whisker input

brne	NEXT		; Continue with next check

rcall	HitRight	; Call the subroutine HitRight

rjmp	MAIN		; Continue with program

NEXT:	cpi	mpr, (1<<WskrL); Check for Left Whisker input

brne	MAIN		; No Whisker input, continue program

rcall	HitLeft		; Call subroutine HitLeft

rjmp	MAIN		; Continue through main

;****************************************************************

;* Subroutines and Functions

;****************************************************************

;----------------------------------------------------------------

; Sub:	HitRight

; Desc:	Handles functionality of the TekBot when the right whisker

;		is triggered.

;----------------------------------------------------------------

HitRight:

push	mpr		; Save mpr register

push	waitcnt		; Save wait register

in	mpr, SREG	; Save program state

push	mpr		;

; Move Backwards for a second

ldi	mpr, MovBck	; Load Move Backwards command

out	PORTB, mpr	; Send command to port

ldi	waitcnt, WTime	; Wait for 1 second

rcall	Wait		; Call wait function

; Turn left for a second

ldi	mpr, TurnL	; Load Turn Left Command

out	PORTB, mpr	; Send command to port

ldi	waitcnt, WTime	; Wait for 1 second

rcall	Wait		; Call wait function

; Move Forward again

ldi	mpr, MovFwd	; Load Move Forwards command

out	PORTB, mpr	; Send command to port

pop	mpr		; Restore program state

out	SREG, mpr	;

pop	waitcnt		; Restore wait register

pop	mpr		; Restore mpr

ret			; Return from subroutine

;----------------------------------------------------------------

; Sub:	HitLeft

; Desc:	Handles functionality of the TekBot when the left whisker

;		is triggered.

;----------------------------------------------------------------

HitLeft:

push	mpr		; Save mpr register

push	waitcnt		; Save wait register

in	mpr, SREG	; Save program state

push	mpr		;

; Move Backwards for a second

ldi	mpr, MovBck	; Load Move Backwards command

out	PORTB, mpr	; Send command to port

ldi	waitcnt, WTime	; Wait for 1 second

rcall	Wait		; Call wait function

; Turn right for a second

ldi	mpr, TurnR	; Load Turn Right Command

out	PORTB, mpr	; Send command to port

ldi	waitcnt, WTime	; Wait for 1 second

rcall	Wait		; Call wait function

; Move Forward again

ldi	mpr, MovFwd	; Load Move Forwards command

out	PORTB, mpr	; Send command to port

pop	mpr		; Restore program state

out	SREG, mpr	;

pop	waitcnt		; Restore wait register

pop	mpr		; Restore mpr

ret			; Return from subroutine

;----------------------------------------------------------------

; Sub:	Wait

; Desc:	A wait loop that is 16 + 159975*waitcnt cycles or roughly

;		waitcnt*10ms.  Just initialize wait for the specific amount

;		of time in 10ms intervals. Here is the general eqaution

;		for the number of clock cycles in the wait loop:

;			((3 * ilcnt + 3) * olcnt + 3) * waitcnt + 13 + call

;----------------------------------------------------------------

Wait:

push	waitcnt		; Save wait register

push	ilcnt		; Save ilcnt register

push	olcnt		; Save olcnt register

Loop:	ldi	olcnt, 224	; load olcnt register

OLoop:	ldi	ilcnt, 237	; load ilcnt register

ILoop:	dec	ilcnt		; decrement ilcnt

brne	ILoop		; Continue Inner Loop

dec	olcnt		; decrement olcnt

brne	OLoop		; Continue Outer Loop

dec	waitcnt		; Decrement wait

brne	Loop		; Continue Wait loop

pop	olcnt		; Restore olcnt register

pop	ilcnt		; Restore ilcnt register

pop	waitcnt		; Restore wait register

ret			; Return from subroutine