Fuses and Lock Bits
The ATMega128 has several special memory areas
-Six lock bits which determine program memory features.
-Three fuse bytes which determine various hardware features
-Three bytes for device signature
-Four bytes for RC oscillator calibration (shared with device signature)
The six lock bits are broken down into:
-four BLB lock bits
-two lock bits for overall programming protection
The lock bits select where the SPM and ELPM are allowed to operate and
if the bootloader is allow to overwrite itself.
Lock bits are logic zero when programmed, one when not programmed

---
The Fuse bytes are the
-Extended Fuse Byte
-Low Fuse Byte
-High Fuse Byte
Extended Fuse Byte determines
-M103C (mega 128 predesessor) compatibility
-if watchdog Timer is always on

---
The Fuse bytes are the
-Extended Fuse Byte
-Low Fuse Byte
-High Fuse Byte
Extended Fuse Byte determines
-M103C (mega 128 predesessor) compatibility
-if watchdog Timer is always on
High Fuse Byte determines
-availability of OCD, JTAG, SPI downloading
-if oscillator options are available
-if EEPROM is preserved during chip erase
-boot block size
-if reset vector is application or bootloader address zero
Fuse bits are logic zero when programmed, logic one when not programmed
Fuse bits are inaccessible by application or bootloader programs
Fuse bits not effected by chip erase or at all if lock bit (LB1) is set

---
High Fuse Byte determines
-availability of OCD, JTAG, SPI downloading
-if oscillator options are available
-if EEPROM is preserved during chip erase
-boot block size
-if reset vector is application or bootloader address zero

---
Low Fuse Byte determines
-brownout detector trigger level
-startup time
-clock sources
Fuse bits are logic zero when programmed, logic one when not programmed
Fuse bits are inaccessible by application or bootloader programs
Fuse bits not effected by chip erase or at all if lock bit (LB1) is set

---
Fuse bytes can be read/written with avrdude interactively in terminal mode
avrdude -p m128 -u -c usbasp -t //unsafe option chosen (see manual)
avrdude: AVR device initialized and ready to accept instructions
avrdude: Device signature = 0x1e9702
avrdude: current erase-rewrite cycle count is 52 (if being tracked)
avrdude> d efuse
>>> d efuse //dump entended fuse
0000 fd
avrdude> d hfuse //dump high fuse
>>> d hfuse
0000 99
avrdude> d lfuse //dump low fuse
>>> d lfuse
0000 e1
avrdude> w efuse 0 0xff //write extended fuse
>>> w efuse 0 0xff
avrdude> w hfuse 0 0x89 //wire high fuse
>>> w hfuse 0 0x89
avrdude> w lfuse 0 0x2f //write low fuse
>>> w lfuse 0 0x2f

---
Fuse bytes (and memory) can be read/written with avrdude from the command line.
For example, when programming a Mega48 to run at 8Mhz, the low fuse needs
to be changed to 0xE2. It can be done like this:
sudo avrdude -c usbasp -p m48 -U lfuse:w:0xE2:m -v
"-U" indicates a memory operation,
"w" indicates a write
"lfuse" the location to perform the operation on
"0xe2" the hex value being written
"m" take the immediate value specified on command line
"-v" verbose mode
Multiple operations can be done simultaneously too:
avrdude -p m128 -u -U flash:w:diag.hex \
> -U eeprom:w:eeprom.hex \
> -U efuse:w:0xff:m \
> -U hfuse:w:0x89:m \
> -U lfuse:w:0x2e:m
Verifying from command line that flash memory is same as the file code.hex:
avrdude -p m128 -c <programmer_type> -U flash:v:code.hex \
See the avrdude manual for more details:
http://www.nongnu.org/avrdude/user-manual/avrdude.html