AVR JTAG Interface
The JTAG (Joint Test Action Group) development started about 1985 as a method
to test populated circuit boards after manufacture.
The majority of manufacturing and field faults in circuit boards were due
to bad solder joints.
JTAG was meant to provide a “pins-out” view from one IC pad to another so all
these faults could be discovered.
Became an IEEE standard in 1990 (IEEE Std. 1149.1-1990)
Now adopted by electronics companies all over the world.
Boundary-scan is mostly synonymous with JTAG.
In many ICs, internal registers are on a scan chain. This allows functionality to
be tested completely even while an IC is in the circuit card and possibly while
in a functioning system.

---
In the most basic implementation,
the boundary that is scanned is the
i/o shell at the periphery of a chip.
The interfaces to the JTAG logic
are very similar to what we have
seen for SPI.....
tck	equiv to	sck
tdi	equiv to	mosi
tdo	equiv to	miso
tms no match
The JTAG scan chain forms a long
shift register.

---
Boundary scan principle of operation - chip level

---
Boundary scan principle of operation - board level

---
JTAG is now primarily used as
-a method to access sub-blocks of integrated circuits
-programming non-volatile memories (EEPROM, Flash)
-a mechanism for debugging embedded systems
-a mechanism for checking for manufacturing defects
As a debugging tool, an in-circuit emulator enables a programmer to
access an on-chip debug module integrated into the CPU.
The debug module enables the programmer to debug the software of an
embedded system by setting breakpoints, view CPU registers and other
internal registers.
The JTAG scan chain generally does not help diagnose or test for
timing, temperature or other dynamic errors.

---
JTAG on the AVR allows access to:
-all internal peripheral units
-internal and external RAM
-internal register file
-program counter
-EEPROM and Flash memory
With the AVR Studio, on chip debug is supported for:
-AVR “BREAK” instruction
-break on change of program memory flow
-single step break
-memory breakpoints
On-chip debug is via private JTAG instructions (Atmel propriatory)

---
ICE with AVR

---
JTAG on the AVR: