Power Management and Sleep Modes
A key feature of many microcontrollers is low power consumption.
The principle way to reduce power consumption is to stop the clock.
Quiescent CMOS consumes essentially no power at feature sizes > .35u
CMOS power dissipation is mostly due to dynamic power dissipation,
i.e., power dissipation caused by signals transitioning.
For example, in the DEC Alpha microprocessor (~1995) approximately
50% of the 30W dissipated was spent in simply driving the clock tree.
Rough figure for power dissipation in CMOS: (neglicting leakage)
Pd = CV2f
where C = capacitance, V = voltage, f = frequency of operation

---
To save power in the AVR: cut off the clock to unused modules
The MCU Control Register holds the power management settings.
MCU Control Register
sleep enable: if set, the MCU will
enter sleep mode when the SLEEP
instruction is executed
SM2 SM1 SM0
  0 0 0	Idle
  0 0 1	ADC noise reduction
  0 1 0	Power Down
  0 1 1	Power Save
  1 0 0	Reserved
  1 0 1	Reserved
  1 1 0	Standby
  1 1 1	Extended Standby

---
Sleep Modes:
Idle Mode:
-Stopped: CPU, Flash memory
-Running: SPI, USART, Comparator, ADC, TWI, TCNT0-3, Watchdog
-Wakeup: external and internal interrupts
ADC Noise Reduction Mode
-Stopped: All above plus the I/O clocks
-Running: ADC, TWI, TCNT0, Watchdog
-Wakeup: external and internal interrupts
Power-down Mode:
-Stopped: All the above plus the external oscillator
-Running: External interrupts, TWI address match, Watchdog
-Wakeup: Watchdog, or brown out reset, external interrupt

---
Power Save Mode: (identical to Power-down, except:)
-Running: TCNT0 also if clocked externally (asynchronous mode)
-Wakeup: can also wakeup from TCNT0 interrupts
Standby Mode: (identical to Power-down except:)
-Running: External crystal clock oscillator still running
-Wakeup: just like Power-down, except wakes up in 6 clock cycles
Extended Standby Mode: (identical to Power-save except:)
-Running: External crystal clock oscillator still running
-Wakeup: just like Power-save, except wakes up in 6 clock cycles