Serial Peripheral Interface (SPI)
SPI = Simple, 3 wire, full duplex, synchronous serial data transfer
Interfaces to many devices, even many non-SPI peripherals
Can be a master or slave interface
4 interface pins:
-MOSI	master out slave in
-MISO	master in slave out
-SCK	serial clock
-SS_n	slave select
3 registers:
-SPCR	control register
-SPSR	status register
-SPDR	data register

---
Full duplex, synchronous serial data transfer
Data is shifted out of the master's (mega128) MOSI pin and in it's MISO pin
Data transfer is initiated by simply writing data to the SPI data register.
All data movement is coordinated by SCK.
Slave select may or may not be used depending on interfacing device.
To get input data only you send “junk” data to SPDR to start the clock.
master SPI device
slave SPI device

---
Slave Select... use it carefully!
In master mode:
-SPI interface has no control of SS_n
-User software has full control of SS_n (Port B, bit 0)
-If configured as output, it’s a general purpose output
-If configured as input, it must be held high, else you will enter slave mode
We will use SPI in master mode, full duplex

---
SPI Control Register (SPCR)
interrupt enable: if set, interrupt
occurs when SPI interrupt flag
and global interrupt enable are set
clock rate
(in SPSR)
spi enable: if set, SPI interface
is enabled
SPI2X SPR1 SPR0 SCLK
0 0 0 fosc/4
0 0 1 fosc/16
0 1 0 fosc/64
0 1 1 fosc/128
1 0 0 fosc/2
1 0 1 fosc/8
1 1 0 fosc/32
1 1 1 fosc/64
data order: if set, LSB is
transmitted first
master/slave select: if set,
SPI in master mode
clock polarity:
'0' SCK low in idle
'1' SCK high in idle
clock phase:
'0' leading edge sample, trailing edge setup
'1' leading edge setup, trailing edge sample

---
SPI Status Register (SPSR)
reserved bits
interrupt flag: set when serial
transfer is complete
write collision: set if SPDR is
written during a receive transfer
2x clock rate: if set, doubles
clock rate in master mode
SPI Data Register (SPDR)
SPDR is a read/write register used for data transfer. Writing SPDR sends data
out MOSI. Reading SPDR gets the data that was clocked into MISO.

---
Mega128 LCD interface
SCK, PB1
LCD strobe, PF3
MOSI, PB2
9-bit shift register
enable pulse generator

---
SPI Application - Code
/*********************************************************************/
// spi_init
//Initializes the SPI port on the mega128. Does not do any further
//external device specific initializations.
/*********************************************************************/
void spi_init(void){
DDRB = 0x07; //Turn on SS, MOSI, SCLK (SS is output)
SPCR = (1<<SPE) | (1<<MSTR); //SPI enabled, master, low polarity, MSB 1st
SPSR = (1<<SPI2X); //run at i/o clock/2
}//spi_init
/***********************************************************************/
// digi_pot_send
//Sends command and data to the digital pot. SPI device chip select is
//active low and is connected to port F bit 2. Total of 16 bits are sent.
//One byte for control and one byte as data passed in.
/***********************************************************************/
void digi_pot_send(uint8_t data){
PORTF &= 0xFB; //port F bit 2, assert active low
SPDR = 0x13; //send command byte (fixed value)
while (bit_is_clear(SPSR,SPIF)) {} //wait till data is sent out
SPDR = data; //send data byte
while (bit_is_clear(SPSR,SPIF)) {} //wait till data is sent out
PORTF |= 0x04; //port F bit 2, deassert to logic high
} //digi_pot_send

---
Typical SPI IC (MCP42010)

---
74HC595 – A perfectly fine SPI peripheral

---
What if you want only to read the SPI port?
To get the SPI clock to run, a "dummy" write is made to the SPI
SPDR register. This starts the clock running so the data on MISO
is brought into the uC.
If no peripherals are selected, the outgoing data will be ignored. If you
are clever, you can send data out and bring data in at the same time.
/*********************************************************************/
// spi_read
//Reads the SPI port.
/*********************************************************************/
uint8_t spi_read(void){
SPDR = 0x00; //"dummy" write to SPDR
while (bit_is_clear(SPSR,SPIF)){} //wait till 8 clock cycles are done
return(SPDR); //return incoming data from SPDR
}//read_spi

---
74HC165 – Another fine SPI peripheral

---
SPI “Gotchas”
“Now my board won’t program.”
SPI shares SCK with programming interface. If it won’t program anymore,
you likely messed up SCK.
“SPI acts totally wierd.”
Often a symptom of SS_n being configured as an input and being left to float
or allowed to go high. SPI goes in and out between slave and master modes.
“I never get data to the SPI device.”
Is clock correctly oriented ? Did you assert the device chip select?
(hint: put SPI write inside a “tight” loop and check with scope. Watch
SCK, data, and chip select)
"SPI device interactions:" When programming, the programmer first does a chip reset. When the mega128 resets, all pins are set to input with high impedance
(floating). If a SPI device is on the SPI bus, its chip-select may
float low and enable the device, and SPI data will crash the programming data. Adding a pull-up resistor to chip selects will solve this problem.