Two Wire Interface
Another popular serial peripheral interface bus
-More flexible than SPI
-Master and slave modes supported
-7-bit slave address
-400khz data xfer speed
-Bidirectional, open-drain bus (device pulls down, resistors pull up)
-Two wires, SCL (clock) and SDA (data)
Typical TWI bus configuration

---
A TWI transmission consists of
-A Start condition
-An address packet consisting of
-Read/Write indication and
 -Slave acknowledge, (SLA+RW)
-One or more data packets
-a Stop condition
A Start condition initiates a transmission by a master.
Between Start and Stop conditions, the bus is busy and no other masters
should try to initiate a transfer.
A Start condition is signaled by a falling edge of SDA while SCL is high.

---
Address packet
-Address packet is 9 bits long
-MSB first
-Address “000 0000” is reserved for broadcast mode
-7 address bits (driven by master)
-1 read/write control bit (driven by master)
-1 acknowledge bit (driven by addressed slave)

---
Data packet
-All data packets are 9 bits long
-MSB first
-One data byte plus an acknowledge
-During a transfer, Master generates SCL, Receiver acknowledges
-Acknowledge (ACK): Slave pulls down SDA in the 9th SCL cycle
-Not Acknowledge (NACK): Slave does not pull down SDA in 9th cycle
NACK
ACK

---
STOP condition
-A Stop condition completes a transmission by a master.
-A Stop condition is signaled by a rising edge of SDA while SCL is high.
SDA
SCL

---
Special cases
-A Repeated Start occurs when the master initiates a new transfer
        without relinquishing control of the bus. Otherwise, this is just
        like another Start.
        SDA
        SCL
-Clock stretching: If a Master is issuing a clock that is too fast, the
Slave can extend the clock by extending the low period of SCL.
-Multiple packets: Several data bytes may be sent between SLA+RW
and Stop conditions.

---
TWI Registers
-TWBR (bit rate register)
-Controls the period of SCL when the TWI module is
        operating in Master mode
-TWAR (address register)
-Used when TWI module is receiving data to identify its address.
-TWCR (control register)
-Controls operation of the TWI unit
-Used to generate START, STOP, ACK pulse
-Also enables TWI operation including interrupt enables
-TWSR (status register)
-Reflects the status of the TWI logic bus via codes.
-Holds the prescale value for the TWI SCL pulse generator
-TWDR (data register)
-In transmit mode, it holds the data to send
-In receive mode, it holds the data received

---
TWI Interrupts
-The TWINT flag in the control register must be cleared by SW
-it is not cleared by the ISR like other interrupt sources
-TWINT indicates that software needs to take care of something
        on the TWI bus.
-One cycle after TWINT asserts, TWSR will hold a status code
        identifying the event that caused the interrupt.
-While TWINT is set, SCL is stretched low and the TWI bus
        is stalled to allow software time to take care of business.
-When TWINT is reset, the bus begins operations again.
-When TWAR, TWSR or TWDR are changed,
TWINT must be logic “1”.

---
TWI Interrupts (cont)
-TWINT is set when the TWI unit:
-finishes sending a Start/Repeated Start
-finishes sending a SLA+RW
-finishes sending an address byte
-looses arbitration
-has been addressed by its slave address or a general call
-has received a data byte
-receives a Stop or Repeated Start while being addressed as a slave
-has a bus error do to illegal Start or Stop conditions
-TWINT is not set after the TWI unit:
-sends the STOP condition

---
Using TWI (assuming its enabled)
if((TWSR & 0xF8) != MT_SLA_ACK)
 error();
TWDR = data;
TWCR = (1<<TWINT)
if((TWSR & 0xF8) != START)
 error();
if((TWSR & 0xF8) != MT_DATA_ACK)
 error();
TWCR = (1<<TWINT) | (1<<TWSTO)
TWCR = (1<<TWINT) |
        (1<<TSWTA)
TWDR = SLA_W;
TWCR = (1<<TWINT)
while(!(TWCR & (1<<TWINT)))
while(!(TWCR & (1<<TWINT)))
while(!(TWCR & (1<<TWINT)))

---
A typical TWI device:
The device is address according
to the manufacturers fixed address
plus the address pin.
The pointer register is used to
read or write the other registers.
Writing to the chip is sometimes a two step process. But, the LM73
pointer register remembers the last pointed to register.

---
LM73: one byte write
 -send device address
 -send pointer address
 -send data value to register
0x00 - temp
0x01 - config
0x04 - ctrl/stat
data
0x90

---
LM73: two byte read with preset pointer
NACK by master indicates
end of reading.
0x91
data
data

---
Gotcha’s with the LM73:
     Don’t take a long time doing stuff while TWINT is asserted.
You may need a short pause between stop an start conditions.
When using 400khz clock, I didn’t. I did with slower clocks!

---
TWI coding
Strongly suggest using twi.h: #include <utils/twi.h>
The #defines there will help make your code readable.
//start condition transmitted
#define TW START	0x08
//repeated start condition transmitted
#define TW_REP_START	0x10
//SLA+W transmitted, ACK received
#define TW_MT_SLA_ACK	0x18
//SLW_W transmitted, NACK received
#define TW_MT_SLA_NACK	0x20
..........

---
TWI coding
Strongly suggest using your own defines too:
//LM73 Addresses on the I2C bus
//Using LM73-0, address pin floating (datasheet pg. 9)
#define LM73_ADDRESS 0x90
#define LM73_WRITE (LM73_ADDRESS | TW_WRITE) //LSB is a zero to write
#define LM73_READ (LM73_ADDRESS | TW_READ) //LSB is a one to read
//define the codes for actions to occur
#define TWCR_START 0xA4 //send start condition
#define TWCR_STOP 0x94 //send stop condition
#define TWCR_RACK 0xC4 //receive byte and return ack to slave
#define TWCR_RNACK 0x84 //receive byte and return nack to slave
#define TWCR_SEND 0x84 //pokes the TWINT flag in TWCR and TWEN
#define LM73_PTR_TEMP 0x00 //LM73 temperature address
#define LM73_PTR_CONFIG 0x01 //LM73 configuration address
#define LM73_PTR_CTRL_STATUS 0x04 //LM73 ctrl and stat register

---
TWI coding
Strongly suggest well structured code with inline debug as needed:
TWCR = TWCR_START; //send start condition
while(!(TWCR & (1<<TWINT))){} //wait for start condition to transmit
if(!(TW_STATUS == TW_START)){
  string2lcd(error1); return(1);}//check start status
TWDR = LM73_WRITE; //send device addr, write bit set
TWCR = TWCR_SEND; //poke TWINT to send address
while(!(TWCR & (1<<TWINT))){} //wait for LM73 address to go out
if(TW_STATUS != TW_MT_SLA_ACK){
  string2lcd(error2); return(1);}//check status reg for SLA+W ACK
TWDR = LM73_PTR_TEMP; //send pointer address to LM73
TWCR = TWCR_SEND; //poke TWINT to send address
while(!(TWCR & (1<<TWINT))){} //wait for LM73 data byte 1 to go out
if(TW_STATUS != TW_MT_DATA_ACK){
  string2lcd(error3); return(1);} //check ack status
TWCR = TWCR_STOP; //finish transaction
return(0); //return success value
}

---
Reading the temperature is a bit funny...
uint8_t rd_temp(){
  TWCR = TWCR_START; //send start condition
   *
  TWDR = LM73_READ; //send device addr, read bit set
  *
*
  TWCR = TWCR_RACK; //receive data byte, return ACK
  while(!(TWCR & (1<<TWINT))){} //wait for data byte to come in
  if(TW_STATUS != TW_MR_DATA_ACK){return(1);} //byte 1 read failure
  lm73_temp_high = TWDR; //store temp high byte
  TWCR = TWCR_RNACK; //recv temp low byte, return NACK
  while(!(TWCR & (1<<TWINT))){} //wait for data byte to come in
  if(TW_STATUS != TW_MR_DATA_NACK){return(1);} //byte 2 read failure
  lm73_temp_low = TWDR; //store temp low byte
  TWCR = TWCR_STOP; //conclude transaction
  return(0); //return success value
}